## Slide 1: Practical SVBRDF Capture in the Frequency Domain
Miika Aittala
Aalto University
NVIDIA Research
Jaakko Lehtinen
Aalto University
NVIDIA Research
Tim Weyrich
University College London

## Slide 2: Introduction
Realistic graphics requires quality content
  Geometry
  Lighting
  Surface materials
Manual creation difficult, expensive
We present a practical method for capturing detailed spatially varying surface appearance
Notes: Thank you for the introduction.
Realistic computer graphics requires not only advanced rendering methods, but also high quality content.
Producing content by hand is difficult and expensive, so it would be desirable to capture it directly from the real world.
We present a method that captures materials accurately using a simple physical setup.

## Slide 3
Flickr user Jacob Whittaker (CC)
Notes: Real-world surface materials exhibit rich spatial variation, as can be seen in these photos.
The precise reflectance model itself is often secondary; it is the spatial variation that gives these surfaces their character.
http://www.flickr.com/photos/45097561@N00/7521440592/in/photolist-csDmfd-gKMfF-3P95a-XYumy-KzJuj-6QRYm4-7qANW6-5jfMa2-9hrWL4-etf1p-6rF7R-4vFTnU-5PcVGd-5PcVf1-5PcVxS-5PcVpL-92exyf-78qgR7-5X3tMB-7zsDNn-3cvzXt-oS9Wf-7up2f-9SwcwX-4mrs4m-95WRQr-4pvsKp-59chzg-83NKB9-6arsus-5rhVmY-7WJL18-ajfKED-83KmQg-83Kq22-4mJvAu-83Koir-6treoT-GfwTZ-dooLWt-4rfB1L-4Wqsc7-4Wmc94-3aUMpr-3aUMqn-mCoLj-huoJZ-5CvXKv-4S2KCB-3MMaP-3MLdi

## Slide 4
Flickr user Serenae (CC)
Notes: http://www.flickr.com/photos/serenae/6804163629/

## Slide 5
Flickr user this is markb (CC)
Notes: http://www.flickr.com/photos/84848927@N00/4525959656/in/photolist-7TWJ8b-39xW7S-4r9za1-b97Zzi-b981ek-b981KM-7eEgVd-4n2z3o-5vG8or-7uHuLi-7uMkSS-7uMkPb-xdhLb-5vJzdS-kz9hV-aAwtja-kztsr-7MY2D1-6m2ip-9TETGZ-8cZV1t-csExqN-pfYDy-4n5Ayy-dhoHp6-bx7Eot-8UNtNB-e75WB4-b1ro48-5kkD8V-f8xap-zn4jV

## Slide 6
Flickr user hungryblank (CC)
Notes: http://www.flickr.com/photos/hungryblank/129549674/

## Slide 7
Flickr user agatauw (CC)
Notes: http://www.flickr.com/photos/21020954@N06/4262195595/in/photolist-7uCSfX-cD9iNY-8xpeey-4td4TQ-4d7efo-Bsoqj-66h41t-5KSust-59LAmz-5ppj8R-6sy5kg-8Vs5pY-4eEAXt-79h39G-axB4y8-3E2D8-DPS7q-82q9bq-6bn41J-ajEnoE-4DMtmp-8zc39f-8z8W7a-8zc2hY-8z8Smt-8z8Vfg-c3YaDo-Bc8TF-4XqF8N-bWabxz-6V7kkF-4ZEini-5jizsS-edjGAi-bAfDnd-gX8a3-bD3Ga2-7TPHP3-4kaczb-Cjpmb-ev9eDH-9gPY8D-5XciYt-292WDQ-uiFmp-7vEw18-6gPzkr-6gTHNA-8s2aGw-ENk9g-7Jnyv6

## Slide 8
Flickr user Mykl Roventine (CC)
Notes: http://www.flickr.com/photos/64419960@N00/2011052257/in/photolist-44HaLM-65QZ6E-6EGQXT-areaX-byNtRa-4TBcXT-2uE3t-2fv4u6-2bbwi-5F4DpJ-Ekuiv-7zUJNY-dA5Ap-9e1TU5-6cBMWN-6e82i6-5gcSh-a5hSa-xsrJj-ny2v7-Dm7ow-8syYVv-7Sc2Vy-8yd73C-nDDA7-3dfZrY-wSER4-5PUQcQ-6UJK3e-7MKp-Etuqx-8HuNZf-4kuQr-fwXjQ-MreDS-8s941G-vm3QB-xst1i-8wnisY-4qyyM5-4FqjxS-4CaNp7-Hty5Q-4C6uwV-7MABf1-6tpogW-9hNGQR-6EMbSj-6m8xoC-6fBL4i-3p3sTF

## Slide 9: Goals
Capture rich spatial reflectance variation
Using standard office hardware only
Output directly usable by modern renderers
Notes: Based on these considerations, our goal is to capture the detailed spatial variation of a parametric BRDF model.
We achieve this using only standard office hardware, and produce output texture maps that are directly usable by modern renderers – in particular, real time rendering.

## Slide 10: Related work
Notes: Let us look at some previous work.

## Slide 11: Custom equipment
Gardner et al. (2003)
Holroyd et al. (2010)
Dong et al. (2010)
Notes: Pretty much all capturing methods are based on emitting light and observing how it interacts with the surface.
Many of the successful previous methods are based on custom hardware.

## Slide 12: Strong priors and heuristics
CrazyBump
  Proprietary heuristics
”Dark is deep”
  E.g. Glencross et al. (2008)
Intrinsic images, user guidance
  AppGen (Dong et al., 2011)
Notes: On the other hand, light-weight methods often produce impressive results, but do not necessarily reproduce the true appearance faithfully.

## Slide 13: Basis illumination
For BRDF measurement
  Sato et al. (2003), Ghosh et al. (2007)
For SVBRDF
  Low-order spherical harmonics (Ghosh et al. 2009, 2010)
Notes: Other work uses continuous illumination for aliasing-free acquisition of BRDFs and SVBRDFs. Our system system extends these approaches.

## Slide 14: Our approach

## Slide 15: Design goals
Capture materials that can be represented as diffuse + specular + normals
No custom hardware
No moving parts
No user intervention
Notes: Our premises are as follows. We assume that the material follows a simple diffuse-specular-normals model.
Our goal is to build a system that requires no custom hardware, moving parts or user intervention during the capture.

## Slide 16
  SLR camera
Monitor as a programmable area light source
Approximately flat material sample
Notes: We use a system shown in this photo.
The flat material sample is placed underneath a tilted LCD monitor.
The monitor displays patterns and the camera records their reflections.

## Slide 17: Near field illumination, fixed camera
Notes: Placing the monitor very close to the sample allows us to observe reflections from a wide range of angles.
However, our method must now explicitly consider the near field illumination effects.
We also observe only a single camera angle. To generalize to novel views, we fit a parametric model to the observed reflection slice.

## Slide 18: Image formation
=
Light rays leave the emitter and find the camera
Importance rays leave the camera and find the emitter
Notes: Let’s have a look at what happens when we take these pictures.
First of all, instead of propagating light, we propagate importance from the camera – as is often done in for example ray tracing.

## Slide 19: Reflection and measurement
=
BRDF slice
emission
=
Diffuse
Specular
Encodes the effect of surface color, glossiness, normals, etc.!
However, cannot be seen directly.
BRDF

## Slide 20: High-level plan
Physical measurement
  Emit patterns, take pictures
Parametric model
  Mimic measurement process computationally
Optimization
  Recover parameters by fitting model to measurements
Notes: 4:00
Our approach is a classical measure-and-fit one.
We obtain physical measurements of the reflectance by emitting patterns from the monitor.
We then fit a parametric model using optimization, to obtain the albedos, glossiness and normals for every surface point.

## Slide 21: Generic approach
Per-point, nonlinear optimization
  Model evaluation in every iteration
General case needs numerical integration
  Prohibitively expensive
=
BRDF slice
emission
=
Notes: The general approach is to solve a per-point non-linear optimization problem, which requires iterative methods that evaluate the BRDF integral in the inner loop. In our setting, this can lead to hundreds of millions of evaluations.
Arbitrary emission patterns and a general BRDF model, however, can only be integrated numerically, which would lead to trillions (or quadrillions) of BRDF evaluations and hence be computationally intractable.
// 512^2 px * 130 patterns * ~8 iters * 5 fd-taps

## Slide 22: Our approach
Joint design of
  emission patterns
  reflectance model
  analytic image formation model
Analytic integration
=
BRDF slice
emission
=
?
?
Notes: To drastically reduce the costs of integration, we jointly design our emission patterns and the computational image formation model.
In effect, the integral can be evaluated with a simple analytic formula. PAUSE.

## Slide 23: Alternatives
Point evaluations
  Aliasing, missed speculars
  Dynamic range
Spherical harmonics
  Require distant spherical illumination
Notes: One simple way to allow for quick reflectance integration would be to use point-shaped illumination.
This approach runs into trouble with sharp speculars, in the form of aliasing and exposure problems.
Other ideas involve for example spherical harmonics. However, they are not suited for our setup because they require distant full spherical illumination.

## Slide 24: Our choice: windowed Fourier basis
Well-behaved with extreme gloss
Albedos, normals and glossiness have simple effects on data
Useful analytic properties
Notes: Our choice is to display windowed Fourier basis functions, which are essentially waves at different frequencies and orientations as seen here.
As continuous patterns, they support almost mirror-like materials. As we will see, the reflectance parameters have a clear effect on the data, and furthermore, allow for efficient analytic integration.

## Slide 31: Note
Remainder of the slides concerns BRDF at a single surface point
Applies to all points separately

## Slide 32: Measurements are point samples of BRDF spectrum
BRDF slice
exp ( -iωTx )
magnitude
phase
=
x-frequency
y-frequency
4 horizontal cycles
16 horizontal cycles
4 diagonal cycles
ω = (4,0)
ω = (16,0)
ω = (4,4)

## Slide 33
=
Log frequency
Diffuse component is low frequency (bump)
Specular peak has power in high frequencies too
Log magnitude
Consider a very glossy BRDF
Significant power remains at highest measured frequencies
extrapolation
=> suffices to observe low frequencies
decay rate ~ glossiness
height ~ albedos
phase ~ normals

## Slide 34: Data fitting
Input: measured point samples of
Unknowns: parameters that generate (albedos, glossiness, normals)
Need to predict from parameters
BRDF slice
Notes: (NOTE when editing/reviewing: notice the fading-out black bars)
8:45

## Slide 35: Efficient Fourier transform
Idea: build BRDF slice as mixtures of 2D Gaussians in monitor plane
  Gaussians have an analytic Fourier transform
Built using Gaussians!
albedos, glossiness, normals
BRDF slice
Notes: Our key insight is that by expressing the BRDF slice as a mixture of Gaussians in the monitor coordinates, we can analytically Fourier transform it, avoiding the expensive numerical integration discussed earlier.
This is because Gaussians have an effective analytic transformation formula.
Our agenda then, for the next few slices, is to construct a model that takes in the unknown parameters, and outputs a mixture of Gaussians that approximates the BRDF slice.

## Slide 36
BRDF slice
=
+
Diffuse
Specular

## Slide 37
Depends on
Known parameters (calibrated)
Camera and monitor position
Surface point
Unknown parameters
Specular albedo
Glossiness
Kurtosis
Normal
Reflection
=
+
Diffuse
Specular

## Slide 38
Reflection
=
+
Diffuse
Specular
Depends on
Known parameters (calibrated)
Camera and monitor position
Surface point
Unknown parameters
Specular albedo
Glossiness
Normal

## Slide 39
Reflection
=
+
Diffuse
Specular
Careful Gaussian approximation of Blinn model
Accounts for translation, scaling and stretching due to near field effects
Gaussian

## Slide 40
Reflection
=
+
Diffuse
Specular
Done!
Product of geometric terms
Inverse square distance
Cosine of angle to screen
Cosine of angle to surface

## Slide 41
Reflection
=
+
Diffuse
Specular
1/D2
cos(screen)
cos(normal)
=
=
Affine
1/D4
=
Affine
+
+
*
(
)
Mixture of Gaussians approximation to 1/D4
Done!

## Slide 42: Complete model
(
)
*
*
BRDF slice
=
+
Diffuse
Specular
Window
Monitor angular emission
distribution

## Slide 43
Affine
+
+
*
(
)
MoG approximation to 1/D4
Window
Monitor
emission
*
*
=
Specular
+
BRDF slice
[
]
Gaussian
Gaussian
Gaussian
Gaussian
Gaussian
Gaussian
Affine

## Slide 44: Optimization
Levenberg-Marquardt, finite differences
Objective = data fit error + priors
Multiresolution scheme
  32 x 32 => 64 x 64 => … => 1024 x 1024
  Data-dependent upsampling scheme
  Data-dependent priors

## Slide 45: Results
Notes: 13:00

## Slide 46
(video)
see project webpage at
https://mediatech.aalto.fi/publications/graphics/FourierSVBRDF/

## Slide 47
Diffuse albedo
Specular albedo
Glossiness
Kurtosis
Normals

## Slide 48
Diffuse albedo
Specular albedo
Glossiness
Kurtosis
Normals

## Slide 49
Diffuse albedo
Specular albedo
Glossiness
Kurtosis
Normals

## Slide 50
Diffuse albedo
Specular albedo
Glossiness
Kurtosis
Normals

## Slide 51
Diffuse albedo
Specular albedo
Glossiness
Kurtosis
Normals

## Slide 52
Diffuse albedo
Specular albedo
Glossiness
Kurtosis
Normals

## Slide 53: Discussion

## Slide 54: Limitations
Near-planar geometry
Diffuse + specular model
Simple heuristic for index of refraction, but some polarization effects baked in
Ground truth
Our result
Failure case: Brushed metal

## Slide 55: Conclusion
Practical physical setup for capturing rich spatially varying surface appearance
Enabled by joint use of Fourier measurements and Gaussian approximations
Will release code and data

## Slide 56
Thank you.